## Slide 1
Sơ đồ kết nối HIL
A1–A3 là tên các bo. Nối theo tên chân ghi trên bo.
A1 BỘ PHÁT
ESP32 DevKit V1
ESP-WROOM-32
GPIO25 / DAC
GND
Micro-USB 5 V
A2 BỘ THU HIL
TMe ESP32-S3 Dev
WROOM-1 N8R8
GPIO1 / ADC1_CH0
ADC 12-bit, atten cao nhất
GND
USB-C 5 V
3V3
GPIO8 / SDA
GPIO9 / SCL
GND
A3 OLED
SSD1306, I²C
VCC / 3V3
SDA
SCL
GND
R1 10 kΩ ±5%
DAC_OUT
ADC_IN
R2 39 kΩ ±5%
C1
100 nF
±20%
50 V
TP1
TP2
TP3
GND / 0 V
3V3_A2
R3 4k7
DNP*
R4 4k7
DNP*
3V3_A2
C2
100 nF / 50 V
sát A3
GND
1. Chấm đen: dây nối. Dây giao nhau không có chấm: không nối.
2. Nếu OLED đã có điện trở kéo lên, để R3/R4 trống (DNP). Điện trở tổng: 1,1–5,1 kΩ; điện dung bus ≤200 pF.
3. Nếu OLED chưa có điện trở kéo lên, lắp R3/R4 = 4,7 kΩ. I²C: 100 kHz. Đặt C1 gần ADC, C2 gần OLED. Cấp USB riêng; không nối 5 V.
4. Đo TP1, TP2 so với TP3. TP2 ≤2,85 V. Hai đường 3,3 V cần nằm trong ±5%.
RF-HIL-001 / Liên kết nguyên mẫu HIL
Rev B / 18-10-2026
Tờ 1 / 1
Duyệt: chưa phê duyệt
NGUYÊN MẪU HIL / Chưa dùng cho sản xuất / Sơ đồ theo module, không phải thiết kế PCB
Notes: RF-HIL-001 Rev B. Module-interface schematic only, not a PCB production release.
Drawing conventions informed by IEC 61082-1:2014 public scope and IEC 60617. No clause-by-clause conformance certification.
https://webstore.iec.ch/en/publication/4469
https://tc3.iec.ch/tc-activity/graphical-symbols-for-diagrams/
GPIO25 DAC: https://docs.espressif.com/projects/esp-idf/en/latest/esp32/api-reference/peripherals/dac.html
GPIO1 ADC1_CH0 and 100 nF: https://docs.espressif.com/projects/esp-hardware-design-guidelines/en/latest/esp32s3/schematic-checklist.html
ADC accuracy guidance states 0..2900 mV at highest attenuation; Arduino measurable range is broader (0..3100 mV). This drawing targets the narrower range.
I2C: https://www.nxp.com/docs/en/user-guide/UM10204.pdf and https://www.ti.com/lit/an/slva689/slva689.pdf
A2 intended purchase is TMe ESP32-S3 Dev (https://www.tme.vn/Products.aspx?CateId=457), not Espressif DevKitC-1. TMe individual product/PDF could not be re-fetched. Verify actual board revision and silk labels before assembly.
OLED pin order and installed pull-ups are not frozen. R3/R4 are optional 4k7 to 3V3_A2. DNP when existing module pull-ups meet the effective resistance and rise-time acceptance conditions. C2 local decoupling is added.
R2 changed 56k to 39k. For ideal DAC output bounded by 3.3 V +5% and resistor tolerances +/-5%, worst ADC_IN is below 2.85 V. Actual DAC source impedance and S3 ADC transfer curve are not modeled.
R1/R2 budget and module prices remain previous estimates. New 39k procurement and optional 4k7 require quotation. Hardware fit and production approval are not complete.

## Slide 2
Phần cứng cần mua
Danh sách cho 1 bộ; giá chưa gồm vận chuyển
RELYFETAL / HIL
CẤU HÌNH REV B
R3/R4 là linh kiện dự phòng, chưa tính giá. Trước khi mua, xác nhận phiên bản bo, nhãn chân và điện trở kéo lên.
02 / 03
BỘ CƠ BẢN, CHƯA GỒM R3/R4
≈622.000₫
SL | Linh kiện / cấu hình | Giá dự kiến
1 | A1 ESP32 DevKit V1 ESP-WROOM-32, Micro-USB | 109.000₫
1 | A2 TMe ESP32-S3 Dev WROOM-1 N8R8, USB-C | 250.000₫
1 | A3 OLED SSD1306, 0,96 in I²C, 3,3 V | 60.086₫
2 gói+ | R1 10 kΩ + R2 39 kΩ, 1/4 W R3/R4 4,7 kΩ dự phòng (để trống mặc định) | ≈5.500₫ + R3/R4
3 món | Tụ C1/C2 100 nF/50 V + breadboard MB-102 Dây Dupont 40 sợi; tụ mua theo gói 10 chiếc | ≈69.900₫
2 | Cáp Micro-USB và USB-A sang USB-C 1 dây mỗi loại, dài 1 m | ≈127.300₫
Notes: Danh sách đã đồng bộ với sơ đồ slide 1: R1=10 kΩ, R2=56 kΩ, C1=100 nF; cầu chia áp đưa tối đa 3,3 V xuống khoảng 2,8 V. N8R8 official board has 8 MB flash + 8 MB PSRAM https://docs.espressif.com/projects/esp-dev-kits/en/latest/esp32s3/esp32-s3-devkitc-1/user_guide_v1.1.html ; GPIO1 is ADC1_CH0 and ADC 12 dB nominal range is about 0–3.1 V https://docs.espressif.com/projects/esp-idf/en/latest/esp32s3/api-reference/peripherals/adc.html . Clone-board pin mapping can vary; verify silkscreen/module before ordering.
KIỂM THỬ MÔ PHỎNG (18/10/2026)
Chạy python3 analysis/hardware_simulator/simulate_hil_rc.py. Mô hình dùng ECG_RECORD_R01/A02 (2.500 mẫu/ca ở 250 Hz), DAC 0–3,3 V lý tưởng, R1=10 kΩ, R2=56 kΩ, C1=100 nF, 12-bit ADC lý tưởng và lệch pha nguồn/thu 0,1–3,9 ms. Kết quả: gain=0,8485; tau=0,848 ms; fc=187,6 Hz; VADC peak danh định 2,800 V, góc R±5% cao nhất 2,841 V. Ở pha 0,1 ms, tương quan dạng sóng với DAC lý tưởng là 0,876 (r01) và 0,754 (a02); khi pha 3,9 ms gần 1. Suy ra điện áp không vượt 3,0 V mục tiêu trong mô hình, nhưng firmware lấy mẫu tự do 250 Hz không đồng bộ, nên kết quả dạng sóng phụ thuộc pha. ADC mean lý tưởng ca a02 ≈2.094 mã, dưới ngưỡng 2.150 của gate hiện tại; gate demo có thể không từ chối ca a02. Đây là mô phỏng tín hiệu và kiểm tra mã, chưa thay thế đo oscilloscope/ADC thật. Firmware hiện tại cũng chưa nạp/chạy TCN thật.
GIÁ TRA CỨU (VNĐ, chưa gồm vận chuyển; giá/biến thể có thể đổi)
J1 Shopee, ESP32 DevKit V1 ESP-WROOM-32, 109.000: https://shopee.vn/ESP32-DevKit-V1-ESP32-WROOM-32-WiFi-Bluetooth-Development-Board-%E2%80%93-Kit-Ph%C3%A1t-Tri%E1%BB%83n-IoT-Ch%C3%ADnh-H%C3%A3ng-i.65776741.42482058047
J2 TMe, ESP32-S3 Dev dựa ESP32-S3-WROOM-1 N8R8, mã trang 2504, 250.000: https://tme.vn/Product.aspx?id=2504
J3 Shopee PCBLab, SSD1306 0.96in 128x64 4-pin, 60.086: https://shopee.vn/M%C3%A0n-h%C3%ACnh-OLED-0.96-inch-I2C-SSD1306-128x64-giao-ti%E1%BA%BFp-I2C-4-ch%C3%A2n-VCC-GND-SCL-SDA-d%C3%B9ng-cho-Arduino-ESP32-STM32-i.1723076079.51514172829
R1 10 kΩ and R2 56 kΩ, carbon film through-hole 1/4 W 5%, Thegioiic 55 each, MOQ 50 each; R2 seller code IC929: https://www.thegioiic.com/dien-tro-56-kohm-1-4w-5-4-vong-mau ; 10 kΩ listing: https://www.thegioiic.com/dien-tro-10-kohm-1-4w-5-4-vong-mau
C1 ceramic 104 100 nF 50 V, Shopee 10 pcs 6.000: https://shopee.vn/T%E1%BB%A5-g%E1%BB%91m-104-100nF-50V-Ceramic-%2810pcs%29-i.29186330.43423148258
Breadboard MB-102 830 tie points, 32.000: https://shopee.vn/Breadboard-MB-102-830-l%E1%BB%97-Nh%E1%BB%B1a-ABS-ch%E1%BA%A5t-l%C6%B0%E1%BB%A3ng-cao-i.120349161.5216095760 ; Dupont 40P, 21 cm, 31.900–39.900: https://shopee.vn/-B%E1%BB%99-S%E1%BB%A3i-D%C3%A2y-N%E1%BB%91i-40P-D%C3%A0i-21Cm-%28-2-%C4%90%E1%BA%A7u-%C4%90%E1%BB%B1c-C%C3%A1i-%29-D%C3%A2y-C%E1%BA%AFm-Test-M%E1%BA%A1ch--i.61435118.25088627856
USB Micro-B data cable 1 m, Shopee 47.880: https://shopee.vn/C%C3%A1p-d%E1%BB%AF-li%E1%BB%87u-s%E1%BA%A1c-nhanh-USB-Micro-USB-1m-i.376801883.28332691601 ; USB-A to USB-C data cable 1 m, USAMS Shopee 79.420: https://shopee.vn/Usams-D%C3%A2y-C%C3%A1p-S%E1%BA%A1c-Nhanh-Truy%E1%BB%81n-D%E1%BB%AF-Li%E1%BB%87u-%C4%90%E1%BA%A7u-USB-Type-C-D%C3%A0i-1M-D%C3%A0nh-Cho-%C4%90i%E1%BB%87n-Tho%E1%BA%A1i-i.408923716.22343546073
ESP32 DAC GPIO25 official source: https://docs.espressif.com/projects/esp-idf/en/latest/esp32/api-reference/peripherals/dac.html ; ESP32-S3 GPIO1 ADC1_CH0 and calibration caution: https://docs.espressif.com/projects/esp-hardware-design-guidelines/en/latest/esp32s3/schematic-checklist.html ; N8R8 ordering code and board USB supply options: https://documentation.espressif.com/esp-dev-kits/en/latest/esp32s3/esp32-s3-devkitc-1/user_guide_v1.1.html
*Total is approximately 622.000 VND including minimum resistor packs; excludes shipping and marketplace promotions.
REV B UPDATE:
RF-HIL-001 Rev B. Module-interface schematic only, not a PCB production release.
Drawing conventions informed by IEC 61082-1:2014 public scope and IEC 60617. No clause-by-clause conformance certification.
https://webstore.iec.ch/en/publication/4469
https://tc3.iec.ch/tc-activity/graphical-symbols-for-diagrams/
GPIO25 DAC: https://docs.espressif.com/projects/esp-idf/en/latest/esp32/api-reference/peripherals/dac.html
GPIO1 ADC1_CH0 and 100 nF: https://docs.espressif.com/projects/esp-hardware-design-guidelines/en/latest/esp32s3/schematic-checklist.html
ADC accuracy guidance states 0..2900 mV at highest attenuation; Arduino measurable range is broader (0..3100 mV). This drawing targets the narrower range.
I2C: https://www.nxp.com/docs/en/user-guide/UM10204.pdf and https://www.ti.com/lit/an/slva689/slva689.pdf
A2 intended purchase is TMe ESP32-S3 Dev (https://www.tme.vn/Products.aspx?CateId=457), not Espressif DevKitC-1. TMe individual product/PDF could not be re-fetched. Verify actual board revision and silk labels before assembly.
OLED pin order and installed pull-ups are not frozen. R3/R4 are optional 4k7 to 3V3_A2. DNP when existing module pull-ups meet the effective resistance and rise-time acceptance conditions. C2 local decoupling is added.
R2 changed 56k to 39k. For ideal DAC output bounded by 3.3 V +5% and resistor tolerances +/-5%, worst ADC_IN is below 2.85 V. Actual DAC source impedance and S3 ADC transfer curve are not modeled.
R1/R2 budget and module prices remain previous estimates. New 39k procurement and optional 4k7 require quotation. Hardware fit and production approval are not complete.